## Slide 1
Naan Mudhalvan
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 2
Module II
Introduction to Sensor Technology
Tektork Private Limited, Coimbatore

## Slide 3
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Definition of Sensors and Transducers
Sensors
A sensor is a device that detects and measures physical phenomena in its environment and converts that information into an electrical signal.
Essentially, it acts as the "eyes and ears" of a system, providing data about the real world.
This data is then sent to a processor, which can be a computer or microcontroller, for analysis and decision-making.
Example: A temperature sensor (thermistor, thermocouple) converts temperature changes into resistance or voltage changes.

## Slide 4
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Transducer
A transducer is any device that converts energy from one form to another. This conversion can be from electrical to non-electrical, or vice versa.
Transducers are used at the boundaries of systems to convert signals into a different form of energy.
All sensors are transducers, but not all transducers are sensors.
A microphone converts sound (acoustic energy) into an electrical signal.
A loudspeaker converts an electrical signal into sound.

## Slide 5
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Aspect | Sensor | Transducer
Definition | A device that detects or measures a physical quantity and converts it into an electrical signal (or readable form). | A device that converts one form of energy into another (not limited to electrical signals).
Function | Sensing (detecting changes in the environment). | Energy conversion (input transducers = sensors, output transducers = actuators).
Scope | Narrow – specifically related to measurement of physical parameters. | Broader – includes sensors and actuators.
Output | Usually gives an electrical signal proportional to the physical quantity. | Can give electrical, mechanical, thermal, acoustic, or other forms of energy.
Examples | Thermistor (temperature sensor), LDR (light sensor), PIR sensor (motion). | Microphone (sound → electrical), Loudspeaker (electrical → sound), Piezoelectric crystal (mechanical → electrical).
Type | Always an input device. | Can be an input device (sensor) or an output device (actuator).
Application | Used for measurement and monitoring. | Used for both measurement and control/actuation.
Sensor Vs Transducer

## Slide 6
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Importance of Sensors
Sensors are vital to modern technology and industry, playing a critical role in automation, safety, and efficiency. Their key importance includes:
Real-Time Data Collection
  Sensors provide continuous, up-to-date data on system conditions, enabling rapid responses to changing situations and improving process control.
Improved Safety
  Monitoring critical parameters helps detect and address hazards early, supports automatic shutdown systems, and reduces risks in dangerous environments.
Process Automation
  By enabling machines to sense and respond to their environment, sensors automate industrial, building, and domestic processes, reducing manual labor and human error.

## Slide 7
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Importance of Sensors Contd..
Higher Product Quality
  With accurate feedback, sensors help maintain consistent product standards by detecting defects and enabling precise adjustments during manufacturing.
Efficiency and Cost Savings
  Sensors help optimize energy use, reduce waste, improve maintenance schedules, and allow for predictive rather than reactive repairs, saving money across sectors.
Enabling Advanced Technologies
  Sensors are foundational for the Internet of Things (IoT), robotics, smart buildings, and autonomous systems, supporting next-generation digital infrastructure.

## Slide 8
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Importance of Sensors Contd..
Facilitating the Internet of Things (IoT)
  Sensors are the foundational technology for the IoT.
  They connect physical devices to the digital world, allowing for the creation of smart homes, smart cities, and industrial automation networks where devices can communicate and make intelligent decisions.

## Slide 9
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors

## Slide 10
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors
Sensors have widespread use, including but not limited to:
Manufacturing/Industrial Automation
  Monitoring temperature, pressure, humidity, pH, vibration, and flow to automate and optimize production lines and ensure safety.
  Pressure sensors: Monitor hydraulic systems and fluid dynamics.
  Vibration sensors: Detect machinery faults before breakdowns.
  Proximity and position sensors: Guide robotic arms and conveyor systems.
  Flow sensors: Control chemical and liquid processes.

## Slide 11
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors
Smart Buildings
  Controlling lighting, HVAC, and security with occupancy, temperature, and motion sensors for energy savings and comfort.
  Motion sensors: Automate lighting, security systems, and energy-saving features.
  Temperature sensors: Regulate HVAC systems for comfort and efficiency.
  Smoke and gas detectors: Alert occupants to fire or leaks.
  Light sensors: Adjust indoor lighting based on ambient conditions.

## Slide 12
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors
Consumer Electronics
  Found in smartphones (gyroscope, accelerometer), wearables (heart rate, step counting), and home appliances (touch and temperature sensors).
  Accelerometers and gyroscopes: Enable screen rotation, gaming, and fitness tracking.
  Touch sensors: Power smartphones, tablets, and smartwatches.
  Biometric sensors: Enable fingerprint and facial recognition.
  Ambient light sensors: Adjust screen brightness automatically.

## Slide 13
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Healthcare
  Biosensors for glucose monitoring, vital sign sensors for ICUs, and diagnostic medical instruments.
  Heart rate and ECG sensors: Monitor vital signs in wearables and hospital equipment.
  Temperature sensors: Track patient health and manage incubators.
  Glucose sensors: Help diabetics manage blood sugar levels.
  Imaging sensors: Power X-rays, MRIs, and ultrasound machines.

## Slide 14
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Automotive and Transportation
  Crash detection, lane guidance, tire pressure monitoring, and self-driving vehicle navigation.
  Parking sensors: Help drivers avoid obstacles.
  Speed and acceleration sensors: Enable ABS and traction control.
  Oxygen sensors: Optimize fuel combustion and reduce emissions.
  Rain sensors: Automatically activate windshield wipers.

## Slide 15
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Environmental Monitoring
  Checking air and water quality, radiation, pollution, and weather stations in cities and the natural environment.
  Air quality sensors: Detect pollutants and allergens.
  Water quality sensors: Monitor contamination in rivers and reservoirs.
  UV sensors: Measure solar radiation for health and energy applications.
  Seismic sensors: Detect earthquakes and structural vibrations.

## Slide 16
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Agriculture and Farming
  Checking Soil moisture and water quality, Ph Level, and weather stations in agriculture and forming.
  Soil moisture sensors: Optimize irrigation and conserve water.
  pH sensors: Monitor soil health for better crop yields.
  Weather sensors: Predict rainfall, temperature, and wind for farm planning.
  Livestock monitoring sensors: Track animal health and movement.

## Slide 17
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Safety and Security
  Fire alarms, gas leak detection, motion-triggered security cameras, and intrusion sensors.
  Motion Sensors: Detect unauthorized movement in restricted areas or during specific hours.
  Door/Window Contact Sensors: Alert when doors or windows are opened unexpectedly.
  Glass Break Sensors: Recognize the sound frequency of breaking glass to trigger alarms.
  Smoke & Gas Detectors: Warn occupants of fire, carbon monoxide, or gas leaks.

## Slide 18
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
  Surveillance Cameras with PIR Sensors: Activate recording only when motion is detected, saving storage and energy.
  Flame & Heat Sensors: Detect fire hazards in factories and chemical plants.
  Vibration Sensors: Monitor machinery for early signs of malfunction or structural instability.
  Proximity Sensors: Prevent accidents by stopping machines when a person or object is too close.
  Leak Detection Sensors: Identify chemical, gas, or water leaks in pipelines and storage tanks.

## Slide 19
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
  Collision Sensors: Trigger airbags and emergency braking systems.
  Blind Spot Sensors: Alert drivers to nearby vehicles outside their field of view.
  Tire Pressure Sensors: Prevent blowouts and improve fuel efficiency.
  Driver Fatigue Sensors: Monitor eye movement or steering patterns to detect drowsiness.
  Surveillance Sensors: Integrated with AI to detect suspicious behavior in public areas.
  Environmental Sensors: Monitor air quality, radiation, or toxic gases in urban zones.

## Slide 20
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
  Emergency Call Buttons with Location Sensors: Help citizens report incidents with precise location tracking.
  Gunshot Detection Sensors: Used in high-risk areas to alert law enforcement instantly.
  Fence Breach Sensors: Alert farmers to intrusions or escaped livestock.
  Weather Sensors: Warn of extreme conditions that could endanger crops or workers.
  Pesticide Level Sensors: Ensure safe application and prevent overexposure.

## Slide 21
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
  Biometric Sensors: Fingerprint, iris, and facial recognition for secure access.
  RFID/NFC Sensors: Control entry to secure zones using smart cards or mobile devices.
  Tamper Sensors: Detect unauthorized access or physical interference with devices.

## Slide 22
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Sensors Cond…
Aerospace/Space Exploration
  Navigation sensors for satellites, spacecraft performance, and atmospheric measurement.
  Altitude and pressure sensors: Guide aircraft navigation.
  Infrared sensors: Enable night vision and heat detection.
  Radar and sonar sensors: Assist in surveillance and mapping.
  Gyroscopic sensors: Stabilize drones and spacecraft.

## Slide 23
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification of Sensors

## Slide 24
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 25
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Passive sensor:
  It does not need any additional energy source and directly generates an electric signal in response to an external stimulus.
  That is, the input stimulus energy is converted by the sensor into the output signal. Most of passive sensors are direct sensors as we defined them earlier.
  Example: a thermocouple, a photodiode, and a piezoelectric sensor.
Active Sensor
  It requires external power for its operation, which is called an excitation signal.
  That signal is modified by the sensor to produce the output signal.
  Example: a thermistor is a temperature sensitive resistor.
  It does not generate any electric signal, but by passing an electric current through it (excitation signal) its resistance can be measured by detecting variations in current and/or voltage across the thermistor.

## Slide 26
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Measurement
Sensors can be classified based on different criteria such as measurement , working principle, output type, and power requirement.
Temperature Sensors
  Measure the degree of hotness or coldness. Examples include thermocouples, thermistors, and resistance temperature detectors (RTDs).
Pressure Sensors
  Measure pressure, typically of gases or liquids. These are used in a variety of applications, from barometric pressure measurement to tire pressure monitoring.

## Slide 27
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Measurement
Proximity Sensors
  Detect the presence of an object without physical contact. Examples include capacitive, inductive, and infrared (IR) sensors.
Force and Weight Sensors
  Measure the force, stress, or weight applied to them. Load cells are a prime example, often used in digital scales.
Motion and Position Sensors
  Measure movement, speed, or location. These include accelerometers, gyroscopes, and linear variable differential transformers (LVDTs).

## Slide 28
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Measurement
Chemical and Gas Sensors
  Detect the presence and concentration of specific chemical compounds or gases.
  Examples include pH sensors and smoke detectors.
Bio-sensors
  Use a biological component (like an enzyme or antibody) to detect specific biological substances, commonly used in medical diagnostics.

## Slide 29
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Working Principle
Resistive
  The sensor's electrical resistance changes in proportion to the physical quantity being measured. Examples: Thermistors (temperature) and strain gauges (force).
Capacitive
  The sensor's capacitance changes due to a change in the physical quantity. These are often used for measuring position, displacement, and fluid levels.
Piezoelectric
  These sensors generate a voltage when mechanical stress or pressure is applied. They are commonly used in accelerometers and microphones.

## Slide 30
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Working Principle
Inductive
  The sensor operates on the principle of electromagnetic induction, where changes in a magnetic field or inductance are used for detection.
  Inductive proximity sensors for metal detection and LVDTs for displacement are good examples.
Hall Effect
  These sensors produce a voltage output when a magnetic field is applied perpendicular to a current-carrying conductor.
  They are used for magnetic field detection, position sensing, and current sensing.

## Slide 31
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Classification based on Working Principle
Optical
  The sensor's operation is based on light and its properties. This can involve measuring light intensity, wavelength, or changes in a light beam.
  Photodiodes and IR sensors fall into this category.
Thermoelectric
  These sensors convert a temperature difference into an electrical voltage.
  Thermocouples are a classic example of this principle.

## Slide 32
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Temperature sensors
  Temperature sensors are devices designed to measure the amount of heat or cold (temperature) in objects, environments, or processes and provide readings in readable units such as Celsius or Fahrenheit.
  They are widely used in electronics, industry, IoT, automotive, HVAC, and biomedical applications.

## Slide 33
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Temperature sensors
LM35
DHT 11
DHT 22
BMP280
DS18B20
Thermistor
MLX90614

## Slide 34
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
Most temperature sensors work by converting thermal changes (heat/coolness) into a corresponding change in electrical properties like resistance, voltage, or current.
For example, the resistance across a thermistor or RTD changes with temperature, while thermocouples generate a voltage proportional to temperature differences (Seebeck effect).

## Slide 35
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Main Types of Temperature Sensors
Contact Sensors
These must be in direct contact with the target. Common examples are:
  Thermocouples:
    Two different metals joined at one end, producing a voltage related to temperature differences. Wide temperature range, generally low accuracy, nonlinear output.
    Made of two different metals joined at one end.
    Generate a voltage based on the temperature difference (Seebeck effect).
    Range: –200 °C to +1750 °C (depending on type: J, K, T, etc.)
    Advantages: Wide range, rugged, inexpensive.
    Disadvantages: Requires reference junction compensation, less accurate than RTDs.

## Slide 36
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
  Resistance Temperature Detectors (RTD):
    Metal resistors (often platinum) whose resistance varies linearly with temperature. Highly accurate and stable, used in critical applications.
    Resistance of metal (usually platinum, like PT100/ PT1000) changes with temperature.
    Range: –200 °C to +850 °C
    Advantages: Very accurate, stable over time.
    Disadvantages: More expensive, slower response.

## Slide 37
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
  Thermistors:
    Typically made from semiconductor material; resistance decreases as temperature rises. NTC (Negative Temperature Coefficient) thermistors are common in consumer electronics and medical devices.
    Semiconductor resistors whose resistance changes non-linearly with temperature.
    Two types: NTC (Negative Temperature Coefficient) and PTC (Positive Temperature Coefficient).
    Range: –100 °C to +300 °C (NTC).
    Advantages: High sensitivity, inexpensive.
    Disadvantages: Limited range, non-linear.

## Slide 38
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Non-Contact Sensors:
These measure temperature by detecting infrared (thermal) radiation.
  Infrared Thermometers/Pyrometers/Thermal Imaging Cameras: Used when contact is unsafe or impractical (hazardous fields, moving objects).
  Non-contact measurement using infrared radiation.
  Examples: MLX90614, FLIR sensors.
  Range: –70 °C to +380 °C (depends on model).
  Advantages: Can measure without touching, useful for moving/hazardous objects.
  Disadvantages: Sensitive to dust, smoke, and emissivity variations.

## Slide 39
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Other Types and Special Features
Semiconductor-Based Sensors:
  Incorporated on IC chips, use matched diode junctions; linear output but less accurate, narrower range, and slower response.
  Glass Thermometers and Fiber Bragg Gratings: Occasionally used in specialized applications
  Use built-in diodes or transistors to measure temperature.
  Available as analog (LM35, TMP36) or digital (DS18B20, TMP102, DHT11/DHT22 for temp+humidity).
  Range: –55 °C to +150 °C.
  Advantages: Easy to interface with microcontrollers, calibrated, compact.
  Disadvantages: Limited range, not as rugged as thermocouples.

## Slide 40
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Temperature Sensors in Electronics/IoT
  LM35, LM75, TMP36 → Simple analog sensors.
  DS18B20 → Digital, 1-Wire protocol, waterproof versions available.
  DHT11 / DHT22 → Combined temperature + humidity sensor.
  BMP280 / BME280 → Temperature, pressure, (and humidity in BME280).
  MLX90614 → IR-based, non-contact.

## Slide 41
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Industrial automation (process control)
  Environmental monitoring
  Consumer electronics (appliances, cars)
  Medical diagnostics and life sciences
  Building and structural monitoring (bridges, dams)
  Safety systems (fire detection)

## Slide 42
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Type | Range (°C) | Accuracy | Responsiveness | Output | Notable Uses
Thermocouple | -200 to 1750 | 0.5–5°C | Fast | Nonlinear | Industrial, high heat
RTD | -200 to 600 | High | Moderate | Linear | Scientific, industrial
NTC Thermistor | -50 to 250 | High | Very fast | Nonlinear | Electronics, HVAC, medical
Semiconductor | -70 to 150 | Moderate | Slow | Linear | Embedded systems, IoT
IR/Pyrometer | Varies | Varies | Fast | Non-contact | Hazardous, remote sensing
Comparative Table

## Slide 43
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Pressure sensors
Pressure sensors are devices that measure the force exerted by a gas or liquid on a surface and convert this mechanical pressure into an electrical signal for monitoring or control purposes.
They are widely used in industrial automation, automotive systems, environmental monitoring, and safety applications.

## Slide 44
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Pressure sensors
BMP280
BMP180
DPS310
MPX5700
MS5611

## Slide 45
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
  A typical pressure sensor includes a sensing element (such as a diaphragm) which deflects when pressure is applied; the amount of deflection is proportional to the pressure's magnitude.
  This mechanical deformation is then converted into an electrical signal through different technologies, such as:
    Strain gauge (piezoresistive): Resistance changes as the diaphragm stretches, measured in volts.
    Capacitive: The diaphragm forms part of a capacitor, and changes in capacitance are detected as the diaphragm moves.
    Piezoelectric: Certain crystals generate a voltage when subjected to mechanical stress.
    Others: Inductive, optical, and resonant types are used in specific applications.

## Slide 46
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Types of Pressure Sensors
Piezoresistive/Strain Gauge
  These are the most common type. They use strain gauges whose electrical resistance changes when they are deformed by pressure on a diaphragm.
  They are robust and accurate, making them suitable for a wide range of industrial and automotive applications.
  Based on Wheatstone bridge with strain gauges.
  Pressure deforms a diaphragm → resistance changes → voltage output.
  Applications: Automotive (engine pressure, tire monitoring), industrial systems.

## Slide 47
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Capacitive
  These sensors measure pressure by detecting changes in electrical capacitance.
  They consist of two plates, one of which is a flexible diaphragm.
  As pressure flexes the diaphragm, the distance between the plates changes, which alters the capacitance.
  They are known for high sensitivity, making them suitable for low-pressure applications.
  High sensitivity, good for low-pressure ranges.
  Applications: Medical devices, HVAC, barometers.

## Slide 48
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Piezoelectric
  These sensors use materials (like quartz) that generate a small electrical charge when subjected to mechanical stress.
  This makes them ideal for measuring rapid, dynamic pressure changes, such as those in engine combustion.
  They cannot measure static pressure because the charge dissipates over time.
  Use piezoelectric crystals → generate charge when pressure is applied.
  Very fast response but not suitable for static measurements (only dynamic).
  Applications: Microphones, accelerometers, engine combustion monitoring.

## Slide 49
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Resonant and Optical Pressure Sensors
Specialized applications such as meteorology or high-temperature environments.
Resonant Pressure Sensors
  Pressure changes natural frequency of a vibrating element.
  Very accurate and stable.
  Applications: Aerospace, precision instruments.
Optical Pressure Sensors
  Use light modulation (fiber optic or interferometry).
  Immune to EMI, works in harsh environments.
  Applications: Oil & gas, biomedical (catheters), aerospace.

## Slide 50
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Pressure Sensors in Electronics/IoT
  BMP180 / BMP280 / BME280 → Barometric pressure + temperature (and humidity in BME280).
  MPX5700, MPX4115A → Automotive pressure sensors.
  MS5611 → High-resolution barometric pressure for drones.
  DPS310 → Ultra-compact digital pressure sensor.

## Slide 51
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
Industrial process control (e.g., hydraulic systems)
Automotive (e.g., tire pressure monitoring, engine boosting)
Medical devices (e.g., blood pressure monitors)
Environmental monitoring (weather stations)
Safety and alarm systems

## Slide 52
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Proximity Sensors
  Proximity sensors are contactless devices that detect the presence or movement of objects within a certain range and convert this information into an electrical signal.
  They are widely used in automation, safety, mobile devices, IoT and process monitoring where non-contact object detection is critical.

## Slide 53
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Inductive Proximity
Capacitive Proximity
Magnetic Proximity
Ultranic Sensor
Optical Proximity
Magnetic Reed Switch
IR Sensor Module

## Slide 54
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
  All proximity sensors operate by sensing changes in some physical property (such as capacitance or magnetic field) when an object approaches the sensor's detection range, outputting a signal when the threshold is crossed.
  Their operation is independent of the object's color, relying only on its movement, material, or other physical characteristics.

## Slide 55
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Types of Proximity Sensors
Inductive Proximity Sensors
  These sensors are used to detect metal objects. They create a magnetic field that is emitted from the sensor face.
  When a metal object enters this field, it causes a change in the field's oscillation, which is detected by the sensor.
  Metal entering the field induces eddy currents that alter the sensor's output.
  Range: typically up to 10 mm.
  Applications: Metal detection in automation, machine tools, conveyor systems, position detection,Counting parts.

## Slide 56
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Capacitive Proximity Sensors
  Sense both metallic and non-metallic objects (including solids, liquids, powders, plastic, glass,wood) by detecting changes in capacitance between the sensor and the target.
  They work by generating an electrostatic field. When an object enters this field, it changes the capacitance between the sensor and its surroundings.
  Capacitive sensors are useful for tasks like detecting the level of liquid in a tank or the presence of a box on a conveyor belt.
  Range: up to ~25 mm.
  Applications: Level detection (liquids, powders), packaging machines.

## Slide 57
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Magnetic Proximity Sensors
  Rely on magnetic fields, typically using Hall effect sensing or reed switches to detect magnetic objects like permanent magnets.
  Hall Effect sensors give digital or analog output based on field strength.
  Applications: Door sensors, speed sensing, smartphones, brushless motors.

## Slide 58
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Optical Proximity Sensors
  Detect objects by using a light emitter and receiver; measure reflected light from the target to identify its presence.
  Types
    Through-Beam: The emitter and receiver are in separate housings, and the object is detected when it breaks the light beam.
    Retro-Reflective: The emitter and receiver are in the same housing, and the object is detected when it interrupts the beam that is bouncing off a special reflector.
    Diffuse-Reflective: The emitter and receiver are in the same housing, and the object is detected when it reflects a portion of the emitted light back to the sensor.
    Applications: Counting objects, safety barriers, smartphones (screen off during calls).

## Slide 59
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Ultrasonic Proximity Sensors
  These sensors use sound waves to detect objects.
  The sensor emits a high-frequency sound pulse (ultrasound) and measures the time it takes for the echo to return.
  By calculating the time of flight, the sensor determines the distance to the object. Can detect solid, liquid, or granular materials.
  Range: a few cm to several meters.
  Applications: Measuring distance ,Parking sensors in cars, robotics obstacle detection, liquid level sensing.

## Slide 60
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Industrial automation (robotic arms, conveyor systems)
  Safety and security (door sensors, presence detection)
  Mobile devices (screen control, user interface)
  Process control (level detection, material handling)

## Slide 61
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Force and weight sensors
Force and weight sensors, often called load cells, are devices that measure force and convert it into a measurable electrical signal. While "force" and "weight" are technically distinct concepts in physics, the sensors that measure them operate on the same fundamental principles because weight is the force of gravity acting on a mass.
Force and weight sensors—including load cells, strain gauge sensors, and force-sensitive resistors.

## Slide 62
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
HX711_Load Cell
Load Cell
Load Cell Module
Force Sensor

## Slide 63
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
How They Work
The most common type of force and weight sensor uses strain gauges. A strain gauge is a resistor that changes its electrical resistance when it is stretched or compressed.
Sensing Body: The sensor has a metal body (often called the "flexure" or "spring element") designed to deform slightly under applied force.
Strain Gauges: Several strain gauges are bonded to this body in specific patterns. When a force is applied (whether it's tension, compression, or shear), the body deforms, and the strain gauges stretch or contract.
Wheatstone Bridge: The strain gauges are wired into an electrical circuit called a Wheatstone bridge

## Slide 64
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
This circuit is highly sensitive to the small changes in resistance of the strain gauges.
Signal Output: As the resistance changes, the voltage output of the Wheatstone bridge changes proportionally. This voltage is then amplified and converted into a digital reading that corresponds to the applied force or weight.

## Slide 65
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Types
Strain Gauge Load Cells:
  For precise industrial and commercial weighing. Common forms are compression, tension, shear, and single-point load cells
  Use strain gauges attached to a deformable element (beam, diaphragm, etc.).
  When a force/weight is applied → material deforms → strain gauge resistance changes → electrical signal.
  Applications: Weighing machines, industrial scales, robotics.
  Advantages: High accuracy, reliable.
  Example: Wheatstone bridge configuration in load cells.

## Slide 66
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Types
Capacitive Force Sensors
  Used where small, precise force readings are needed, e.g., touch screens.
  Force deforms a diaphragm, changing capacitance between plates.
  Compact and sensitive.
  Applications: Touch sensors, robotics grippers, biomedical devices.

## Slide 67
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Types
Piezoelectric Sensors
  Ideal for dynamic measurements and high-speed force applications.
  Use piezoelectric materials (quartz, PZT) that generate voltage when force is applied.
  Good for dynamic force measurements (fast changes).
  Not ideal for static weight measurement (charge leaks over time).
  Applications: Impact testing, vibration monitoring, automotive crash tests.

## Slide 68
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Types
Hydraulic and Pneumatic Load Cells
  Suited for rugged and heavy-duty weighing, especially where electrical power is unreliable or absent.
  Force compresses fluid → pressure change is measured.
  Rugged, used for very large loads.
  Applications: Heavy-duty industrial weighing, truck scales.

## Slide 69
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Types
Force-Sensing Resistors (FSRs)
  Change resistance as force is applied; useful in tactile and low-force applications.
Magnetic / Electromagnetic Force Sensors
  Use changes in magnetic field when force displaces a magnetic element.
  Less common but used in specialized cases.

## Slide 70
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Examples
  HX711 + Load Cell → Widely used in Arduino/ESP32 IoT weighing projects.
  Strain Gauge Beam Load Cell → Kitchen scales, luggage scales.
  Piezoelectric Discs → Force-sensitive applications.

## Slide 71
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Weighing scales (industrial, retail, personal)
  Robotics, prosthetics, and medical devices
  Material testing, manufacturing quality control
  Automotive (e.g., brake and seatbelt force monitoring)
  Smart appliances and consumer electronics

## Slide 72
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Motion and position sensors
  Motion and position sensors are devices that detect movement, displacement, or the location of an object and convert that information into an electrical signal.
  While they are often discussed together, they serve different primary functions.
  Motion sensors detect whether an object is moving or not, while position sensors measure the specific location or displacement of an object.
  They are essential in industrial automation, robotics, automotive systems, medical devices, and consumer electronics.

## Slide 73
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
MPU 6050
6-axis (Gyro + Accel)
MPU 9250
9-axis (Gyro + Accel + Magn)
BNO055
Orientation
Ultrasonic (HC-SR04)
PIR modules (HC-SR501)
ADXL375
( Accel)

## Slide 74
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Motion Sensors
  Motion sensors detect movement within a specific area and are commonly used for security systems and automated lighting.
  They typically provide a simple binary output: either an object is moving (ON) or it is not (OFF).

## Slide 75
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Types of Motion Sensors
Passive Infrared (PIR):
  These sensors detect the heat (infrared radiation) emitted by a living body.
  When a warm body moves into the sensor's field of view, it causes a change in the detected IR energy, triggering the sensor.
  Detect human/animal motion by sensing IR radiation changes.
  PIR sensors are common in home security systems and automatic lights.
  Applications: Security systems, automatic lights.

## Slide 76
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Ultrasonic:
  These sensors emit high-frequency sound waves and measure the time it takes for the waves to bounce back.
  The sensor detects motion by analyzing changes in the echo, which indicates a moving object. They are often used in automatic doors and parking sensors.
  Applications: Obstacle detection, intrusion alarms.

## Slide 77
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Accelerometers
  Measure acceleration along axes and, by integration, can track movement, tilt vibration.
  Widely used in smart devices and vehicle systems.
  Can detect orientation (tilt with respect to gravity).
  Examples: ADXL345, MPU6050 (accelerometer + gyroscope).
  Applications: Smartphones (screen rotation), vibration monitoring, fitness trackers.

## Slide 78
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Gyroscopes
  Measure angular velocity; used alongside accelerometers for full motion tracking (e.g., IMUs).
  Often combined with accelerometers for 6-DOF motion sensing.
  Applications: Drones (stability), navigation systems, VR controllers.

## Slide 79
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Fibre Optic Sensors
  Use light in optical fibers; resilient to electromagnetic noise and suited for structural or remote monitoring.
Microwave:
  Similar to ultrasonic sensors, these emit microwave radiation and detect motion based on the Doppler effect, which is a change in the frequency of the reflected waves caused by a moving object.
  They can cover large areas and can even "see" through some non-metallic walls.

## Slide 80
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Types of Position Sensors
Potentiometers
  These are contact-based sensors that use a sliding or rotating contact (a "wiper") on a resistive track.
  As the object moves, the wiper's position changes, altering the resistance and producing a proportional voltage output.
  Applications: Joysticks, volume controls, robotic arms.

## Slide 81
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Linear Variable Differential Transformer (LVDT)
  An LVDT is a highly accurate, non-contact sensor(Electromagnetic Transducer) used for measuring linear displacement.
  It consists of a movable magnetic core inside three coils.
  When the core moves, it changes the voltage induced in the secondary coils, providing an output signal proportional to its position.
  Applications: Aerospace, industrial machinery, research labs.

## Slide 82
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Hall Effect Sensors
  These sensors detect changes in a magnetic field. When a magnet attached to a moving object passes by the sensor, it changes the magnetic field, and the Hall effect sensor produces a voltage output that corresponds to the object's position.
  They are non-contact and immune to dirt and debris.
  Applications: Wheel speed detection, brushless DC motor commutation, automotive position sensing.

## Slide 83
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Encoders
  Encoders are used to measure position and speed, especially rotation.
  They consist of a rotating disk with a coded pattern (either optical or magnetic) that is read by a sensor.
  By counting the pulses or reading the pattern, the encoder can determine the exact angular position of a shaft.
Types:
  Rotary Encoders (absolute or incremental) → detect shaft rotation.
  Linear Encoders → detect linear displacement.
  Applications: CNC machines, robotics, industrial automation.

## Slide 84
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Optical Encoders/Sensors
  Rely on changes in light interruption or reflection to accurately determine linear or rotational position; critical for robotics and precise CNC machines
  Use light interruption/reflection to detect position.
  Applications: Printers, optical mice, robotics.

## Slide 85
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Combined Motion & Position Sensors in IoT
  MPU6050 / MPU9250 → Accelerometer + Gyroscope (+ Magnetometer).
  BNO055 → 9-axis absolute orientation sensor.
  PIR modules (HC-SR501) → Motion detection.
  Ultrasonic (HC-SR04) → Distance + movement tracking.

## Slide 86
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Robotics, automation, and precision manufacturing
  Vehicle and drone navigation (steering, stability, safety)
  Process control and level/distance measurement
  Smart devices (cell phones, gaming, wearables)
  Medical diagnostics and patient monitoring

## Slide 87
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Chemical and Gas Sensors
  Chemical and gas sensors are devices that detect and measure the presence and concentration of gases or chemical substances in the environment by converting chemical interactions into electrical signals.
  They are vital in safety, environmental monitoring, industrial automation, healthcare, and IoT applications.

## Slide 88
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
MQ - 2
MQ - 3
MQ - 7
MQ - 135

## Slide 89
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
CCS811
MCS 6814
SCD30
MH-Z19

## Slide 90
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
  Most chemical and gas sensors operate by using a sensing element that changes its physical or electrical properties when it interacts with the target substance.
  This change is then converted into a measurable electrical signal.
The specific mechanism varies depending on the sensor type:
Change in Resistance
Many sensors, like metal oxide semiconductor (MOS) sensors, have a sensing layer whose electrical resistance changes when gas molecules adsorb onto its surface.

## Slide 91
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Electrochemical Reaction
  In electrochemical sensors, the target gas undergoes an oxidation or reduction reaction at an electrode, generating an electrical current proportional to the gas concentration.
Absorption of Light
  Infrared (IR) gas sensors work by shining an IR light beam through a gas sample.
  The sensor measures how much of the light is absorbed, as each gas absorbs specific wavelengths of infrared light.
Catalytic Reaction
  Catalytic bead sensors detect combustible gases. They contain a heated element with a catalyst that causes the gas to burn.
  The heat from this reaction changes the element's resistance, which is then measured.

## Slide 92
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Types of Sensors
Gas Sensors
Gas sensors are designed to detect a specific type or a narrow range of gases.
Semiconductor (MOS) Sensors
  These are a very common and inexpensive type used for detecting gases like carbon monoxide (CO), methane, and volatile organic compounds (VOCs).
  Electrochemical Sensors: Known for their high accuracy and low power consumption, these are often used to detect toxic gases like carbon monoxide and hydrogen sulfide (H2​S) at low concentrations.
  Examples: MQ-series (MQ-2, MQ-3, MQ-7, MQ-135).
  Applications: LPG, methane, alcohol, smoke, air quality monitoring.

## Slide 93
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Catalytic Sensors
  Primarily used to detect flammable gases like propane and methane by measuring the heat generated when the gas burns on a catalytic bead.
Infrared (IR) Sensors
  These are highly selective, long-lasting, and immune to "poisoning" from other chemicals.
  They are ideal for detecting gases that absorb IR light, such as carbon dioxide (CO2​) and hydrocarbons.
  Non-dispersive infrared (NDIR) sensors use light absorption differences to quantify gas concentration.
  Applications: CO₂ monitoring in HVAC, greenhouses, industrial safety.

## Slide 94
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Chemical Sensors
Chemical sensors are a broader category that can include gas sensors but also devices for detecting liquid or solid chemicals.
Biosensors
  These are highly specific sensors that use a biological component, like an enzyme or antibody, to detect a specific chemical or biological substance.
  They are widely used in medical diagnostics to measure blood glucose, for example.
Optical Sensors
  These use light to analyze chemical properties. An example is a colorimetric sensor, which changes color in the presence of a specific chemical, and the color change is measured by a detector.

## Slide 95
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Potentiometric Sensors
  These measure the electrical potential or voltage of a solution to determine the concentration of a specific ion.
  A pH meter is a classic example of a potentiometric chemical sensor.
Electrochemical Sensors
  Use electrodes and electrolytes where the target gas undergoes oxidation or reduction reactions.
  The resulting flow of ions and electrons produces a current proportional to gas concentration.
  Used for toxic gas detection such as CO, H2S, and oxygen levels.

## Slide 96
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Catalytic (Pellistor) Sensors
  Work by oxidizing combustible gases on a catalyst, releasing heat that changes a sensor bead’s resistance.
  Used for flammable gases detection in hazardous environments.
  Detect combustible gases (LPG, methane, hydrogen) by oxidizing them on a heated catalyst → changes resistance.
  Rugged, but require oxygen to operate.
  Applications: Gas leak detectors, mining safety.

## Slide 97
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Chemical & Gas Sensors in IoT/Embedded Systems
  MQ-2 → LPG, methane, smoke.
  MQ-3 → Alcohol detection (breathalyzer).
  MQ-7 → Carbon monoxide (CO).
  MQ-135 → Air quality (NH₃, NOx, benzene, CO₂).
  CCS811 → Indoor air quality (eCO₂, TVOCs).
  MH-Z19 / SCD30 / Senseair → CO₂ NDIR sensors.
  MiCS-6814 → Multiple gases (CO, NO₂, NH₃).

## Slide 98
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Industrial safety (toxic and combustible gas detection)
  Environmental monitoring and air quality control
  Medical diagnostics (oxygen sensors, anesthesia monitoring)
  HVAC and building automation
  Automotive emissions control and detection

## Slide 99
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Biosensors
  A biosensor is an analytical device that detects a specific biological or chemical substance, known as an analyte, and converts its presence or concentration into a measurable electrical or optical signal.
  They combine a biological recognition element with a physicochemical transducer.

## Slide 100
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
The basic principle of a biosensor involves three main parts:
Bioreceptor
  This is the biological component, such as an enzyme, antibody, nucleic acid (DNA), or even a living cell.
  Its job is to specifically bind to or interact with the target analyte. This interaction is the key to the sensor's high selectivity.
Transducer
  This component converts the biological event (the interaction between the bioreceptor and the analyte) into a quantifiable signal.
  For example, a transducer might detect a change in electrical current, light absorption, or heat generated by the reaction.

## Slide 101
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Working Principle
Electronic System
  This part processes the signal from the transducer, amplifies it, and displays the result in a user-friendly format, such as a number on a screen.
Common transducer mechanisms include electrochemical, optical, piezoelectric, and thermal signals.

## Slide 102
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Components
  Analyte: The substance to be measured (e.g., glucose, toxins, pathogens).
  Bioreceptor: Enzymes, antibodies, DNA, cells, or aptamers that selectively bind the analyte.
  Transducer: Converts biochemical response into measurable signals.
  Electronics: Amplifies and processes the transduced signal.
  Display: Presents results to the user clearly.

## Slide 103
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Types of Biosensors
Electrochemical Biosensors
  Measure current, voltage, or impedance caused by biochemical reactions.
  Examples: Glucose sensors, lactate sensors.
  Applications: Diabetes monitoring, blood chemistry analysis.
Optical Biosensors
  Use light absorption, fluorescence, or surface plasmon resonance (SPR).
  Examples: DNA hybridization sensors, immunosensors.
  Applications: Pathogen detection, cancer diagnostics.

## Slide 104
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Thermal Biosensors
  Measure heat generated or absorbed during biochemical reactions.
  Applications: Metabolic activity monitoring, enzyme assays.
Piezoelectric / Mass-based Biosensors
  Detect changes in mass or resonance frequency when biomolecules bind.
  Examples: Quartz Crystal Microbalance (QCM).
  Applications: Viral/bacterial detection, biomarker sensing.
Wearable Biosensors
  Integrated into wearable devices → measure physiological parameters.
  Examples: Sweat sensors, heart rate monitors, oxygen saturation (SpO₂) sensors.

## Slide 105
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications
  Medical diagnostics (glucose monitoring, pathogen detection)
  Environmental monitoring (pollutant detection)
  Food safety and agriculture
  Biotechnology and pharmaceutical research
  Wearable health devices

## Slide 106
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Signal Conditioning of Sensors and Transducers
Op-amps can be used to provide amplification of signals when connected in either inverting or non-inverting configurations.
The very small analogue signal voltages produced by a sensor such as a few milli-volts or even pico-volts can be amplified many times over by a simple op-amp circuit to produce a much larger voltage signal of say 5v or 5mA that can then be used as an input signal to a microprocessor or analogue-to-digital based system.
Therefore, to provide any useful signal a sensors output signal has to be amplified with an amplifier that has a voltage gain up to 10,000 and a current gain up to 1,000,000 with the amplification of the signal being linear with the output signal being an exact reproduction of the input, just changed in amplitude.

## Slide 107
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Signal Conditioning of Sensors and Transducers Contd..
Then amplification is part of signal conditioning. So when using analogue sensors, generally some form of amplification (Gain), impedance matching, isolation between the input and output or perhaps filtering (frequency selection) may be required before the signal can be used and this is conveniently performed by Operational Amplifiers.
Also, when measuring very small physical changes the output signal of a sensor can become “contaminated” with unwanted signals or voltages that prevent the actual signal required from being measured correctly.
These unwanted signals are called “Noise“. This Noise or Interference can be either greatly reduced or even eliminated by using signal conditioning or filtering techniques as we discussed in the Active Filter tutorial.

## Slide 108
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Signal Conditioning of Sensors and Transducers Contd..
By using either a Low Pass, or a High Pass or even Band Pass filter the “bandwidth” of the noise can be reduced to leave just the output signal required.
For example, many types of inputs from switches, keyboards or manual controls are not capable of changing state rapidly and so low-pass filter can be used.
When the interference is at a particular frequency, for example mains frequency, narrow band reject or Notch filters can be used to produce frequency selective filters.

## Slide 109
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Typical Op-amp Filters
Were some random noise still remains after filtering it may be necessary to take several samples and then average them to give the final value so increasing the signal-to-noise ratio.
Either way, both amplification and filtering play an important role in interfacing both sensors and transducers to microprocessor and electronics based systems in “real world” conditions.

## Slide 110
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Signal Conditioning
Sensor signal conditioning involves various techniques to prepare sensor outputs for accurate measurement, processing, and analysis.
The main goal is to take raw sensor signals and make them suitable for use by data acquisition systems, controllers, or digital processors.
Signal Conditioning Techniques
  Amplification
  Filtering
  Isolation
  Linearization
  Excitation
  Conversion
  Temperature Compensation

## Slide 111
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Signal Conditioning Techniques
Amplification
  Boosts weak sensor signals, such as those from strain gauges or load cells, to a level suitable for measurement. Instrumentation amplifiers or differential amplifiers are commonly used to enhance signal strength while minimizing noise and interference.
  Boosts small signals to a measurable range.
  Example: Thermocouple (mV output) → amplified to volts.
  Circuit: Operational Amplifiers (Op-Amps).

## Slide 112
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Filtering
  Removes unwanted noise or frequency components from the sensor output. Filters can be low-pass, high-pass, band-pass, or band-reject depending on the signal and application. Filtering helps in stabilizing signals and improving measurement accuracy.
  Low-pass filters → remove high-frequency noise.
  High-pass filters → remove DC offsets.
  Band-pass filters → extract desired frequency band.

## Slide 113
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Isolation
  Electrically isolates the sensor signal path to prevent ground loops, voltage surges, and interference. This is crucial for maintaining signal integrity, especially in industrial and high-voltage environments.
  Protects system and avoids ground loops.
  Achieved with opto-isolators or transformers.

## Slide 114
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Linearization
  Corrects non-linear sensor outputs so that the signal accurately corresponds to the measured parameter in a linear manner. This processing can be performed using specialized circuitry or software.
  Many sensors have non-linear response (e.g., thermistors).
  Signal conditioning circuits or software can map it to a linear scale.

## Slide 115
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Excitation (Biasing/Powering the Sensor)
  Provides necessary power (voltage or current) to active sensors, such as RTDs or strain gauges, which require external excitation to function correctly.
  Some sensors (e.g., strain gauges, RTDs) require an external excitation voltage or current source.

## Slide 116
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Conversion - Analog-to-Digital Conversion (ADC)
  Converts the sensor output signal from one form to another to ensure compatibility with the next stage of processing. This includes analog-to-digital conversion (ADC) for digital processing or voltage-to-current conversion for transmission.
  Converts conditioned analog signals into digital format for microcontrollers.
  Often integrated into signal conditioning systems.

## Slide 117
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Temperature Compensation
  Adjusts for variations in sensor output caused by temperature changes to maintain consistent accuracy.

## Slide 118
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of Signal Conditioning
  Signal conditioning circuits are essential in a wide variety of industries and applications:
  Industrial weighing systems (load cells)
  Pressure and temperature measurement
  Vibration analysis and structural monitoring
  Medical instrumentation
  Automotive testing
  Environmental and agricultural monitoring

## Slide 119
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Signal Conditioning is Essential
Without proper signal conditioning, the raw data from a sensor can be unusable. It ensures that the signal is:
  Compatible: It matches the voltage and current requirements of the next stage (e.g., an ADC).
  Clean: Unwanted noise and interference are removed.
  Accurate: The signal is a true and correct representation of the physical quantity being measured.
  Safe: It protects sensitive and expensive data acquisition equipment from potential damage.

## Slide 120
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Amplification
  Amplification is the process of increasing the amplitude of a sensor's output signal. Many sensors, particularly those measuring physical quantities like temperature, pressure, or strain, produce very weak signals, often in the millivolt or microvolt range.
  These low-level signals are susceptible to noise and are often too small to be directly processed by an analog-to-digital converter (ADC), which typically has a specific input voltage range (e.g., ±5 V).

## Slide 121
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Amplification serves two primary purposes:
Voltage Level Matching:
  It boosts the signal's voltage to the required level for the ADC, preventing inaccurate readings or potential damage to the converter.
Improving Signal-to-Noise Ratio (SNR)
  By increasing the signal's amplitude, amplification makes it stronger relative to the inherent electronic noise in the system.
  This leads to a higher SNR, which in turn results in more accurate and reliable measurements.

## Slide 122
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Operational Amplifiers (Op-Amps)
  Widely used due to their versatility, high input impedance, and low output impedance. They can be configured to provide precise gain and filtering.
Instrumentation Amplifiers
  Specialized for sensor conditioning, they provide high gain, excellent noise rejection, and differential signal amplification which is useful in noisy environments.
Gain Control
  The amplifier gain determines the extent of signal amplification. Too much gain can saturate the amplifier, while too little may yield poor signal resolution.

## Slide 123
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Filtering
  Filtering is the process of removing unwanted frequency components, or noise, from a sensor signal.
  All electronic signals are susceptible to noise from various sources, such as ambient electromagnetic interference (EMI) or the sensor's own internal electronics.
  This noise can obscure the true signal, leading to inaccurate readings.
There are several types of filters, each designed to address different types of noise:
  Low-pass filters
  High-pass filters
  Band-pass filters
  Notch filters

## Slide 124
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Low-pass filters
  Low-pass filters allow low-frequency signals (the desired signal) to pass while attenuating high-frequency noise.
  This is the most common type of filter used in sensor applications, as most physical phenomena change relatively slowly.
High-pass filters
  High-pass filters allow high-frequency signals to pass while blocking low-frequency signals.
  These can be used to remove unwanted DC offsets or slow-changing drift from a signal.

## Slide 125
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Band-pass filters
  Band-pass filters allow a specific range of frequencies to pass while rejecting frequencies both above and below that band.
Notch filters
  Notch filters are a type of band-stop filter that rejects a very narrow band of frequencies.
  They are particularly useful for removing specific, known noise frequencies like 50/60 Hz power line noise.

## Slide 126
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Filtering can be implemented using either analog circuits (resistors and capacitors) or digital signal processing (DSP) after the signal has been digitized.
Analog filtering is often performed before amplification to remove as much noise as possible before the signal is boosted.
Reduces noise picked up from electromagnetic interference (EMI) or other sources.
Prevents aliasing in analog-to-digital conversion by limiting the bandwidth.

## Slide 127
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Analog-to-Digital Conversion (ADC)
Analog-to-Digital Conversion (ADC) is a critical step in sensor signal conditioning that transforms a continuous analog signal into a discrete digital one.
This conversion is necessary because most modern microcontrollers and digital processors only understand binary data (0s and 1s).
The ADC acts as the bridge, allowing the conditioned sensor signal to be read, stored, and analyzed by a digital system.

## Slide 128
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
The conversion process involves two key steps:
sampling and quantization.
Sampling
The ADC doesn't read the analog signal continuously.
Instead, it takes "snapshots" or samples of the signal's voltage at regular, precise time intervals.
The sampling rate (or sampling frequency) determines how often these snapshots are taken, and it's measured in samples per second (SPS) or hertz (Hz).
According to the Nyquist-Shannon sampling theorem, the sampling rate must be at least twice the highest frequency component of the analog signal to accurately reproduce it digitally and avoid an issue called aliasing.

## Slide 129
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Quantization
Once a sample is taken, the ADC approximates its continuous voltage value to the nearest discrete level.
The number of available discrete levels is determined by the ADC's resolution, which is expressed in bits.
An n-bit ADC has 2n distinct output levels. For example, a 10-bit ADC has 210=1024 possible output values, from 0 to 1023.
Higher resolution means more discrete levels, which results in a more precise digital representation of the analog signal and less quantization error.

## Slide 130
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Input Range Matching
  The sensor signal conditioning amplifies and scales the sensor output to match the ADC input range, maximizing use of the full range for better resolution and accuracy.
Anti-aliasing Filtering
  Before conversion, low-pass filters remove high-frequency noise that could interfere with sampling, preventing distortion in digital output.

## Slide 131
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
ADC Characteristics
Resolution:
  The number of bits in the ADC's output, which determines the precision of the conversion.
  A higher-bit ADC provides a more accurate digital representation.
Sampling Rate:
  The speed at which the ADC takes samples.
  A higher sampling rate is needed for fast-changing signals (high-frequency signals) to prevent data loss or distortion.

## Slide 132
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Accuracy and Linearity:
These parameters describe how well the ADC's digital output corresponds to the actual analog input.
Integral Nonlinearity (INL) and Differential Nonlinearity (DNL) are common metrics used to measure an ADC's linearity.

## Slide 133
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common ADC Architectures for Sensor Systems
Different ADC architectures offer trade-offs between speed, resolution, power consumption, and cost.
Successive Approximation Register (SAR) ADC
This is one of the most common types. SAR ADCs are versatile, offering a good balance of speed (up to a few Msps) and resolution (typically 8 to 16 bits).
They're widely used in a variety of midrange applications.

## Slide 134
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Delta-Sigma (ΔΣ) ADC
This architecture excels at high-resolution conversions (up to 24 bits or more) for low-speed, low-frequency signals.
They use oversampling and noise shaping to achieve high accuracy, making them ideal for precision applications like temperature or weight measurements.
Flash ADC
Known for its extreme speed (hundreds of Msps or even Gsps), the Flash ADC is the fastest type of converter.
However, it requires a large number of components, making it expensive and power-hungry. It's used in high-frequency applications like digital oscilloscopes or high-speed data acquisition.

## Slide 135
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Parameter | Description
Resolution | Number of bits (e.g., 12-bit ADC gives 4096 levels)
Sampling Rate | How often the signal is sampled (Hz)
Input Range | Voltage range the ADC can accept
Accuracy | How close the digital value is to the actual signal
SNR | Signal-to-noise ratio, critical for precision
Important ADC Specs

## Slide 136
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Digital Signal Processing (DSP) for Sensors
Digital Signal Processing (DSP) involves the numerical manipulation of signals after they have been converted from analog to digital form.
For sensors, DSP plays a crucial role in enhancing, analyzing, and interpreting sensor data to improve accuracy, reliability, and functionality.
DSP techniques can be applied to:
  Filter out noise
  Extract features
  Compress data
  Detect patterns or anomalies
  Improve accuracy and reliability

## Slide 137
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
DSP Techniques for Sensors
Technique | Purpose | Example Use Case
Filtering | Removes unwanted noise or interference | Low-pass filter for ECG signals
Fourier Transform (FFT) | Converts signal to frequency domain | Vibration analysis in motors
Windowing | Reduces spectral leakage in FFT | Audio signal analysis
Decimation & Interpolation | Adjusts sampling rate for efficiency | Downsampling accelerometer data
Feature Extraction | Identifies key signal characteristics | Gesture recognition from IMU sensors
Adaptive Filtering | Dynamically adjusts to changing conditions | Noise cancellation in microphones

## Slide 138
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Applications of DSP for Sensors
Advanced Filtering
  While analog filters are limited, DSP enables the creation of highly precise and configurable digital filters.
  These can effectively remove a wide range of noise types and are essential for isolating the desired signal from complex background noise.
  For example, a notch filter can be used to specifically remove 50/60 Hz power line noise from a biomedical sensor signal like an ECG.

## Slide 139
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Linearization and Calibration
  Many sensors have a non-linear response. Instead of using complex analog circuits, DSP algorithms can correct for this non-linearity with high precision.
  They can also perform calibration, adjusting the sensor's output to account for environmental factors, aging, or manufacturing variations, ensuring consistent and accurate readings over time.

## Slide 140
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Frequency Analysis
  The Fast Fourier Transform (FFT) is a fundamental DSP algorithm that converts a signal from the time domain to the frequency domain.
  This is invaluable for applications like vibration analysis, where identifying specific frequency components can help diagnose mechanical issues in a machine.

## Slide 141
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Fusion
  In many modern systems, data is collected from multiple sensors (e.g., an accelerometer, gyroscope, and magnetometer in a smartphone).
  DSP is used to fuse this data, combining the individual readings to provide a more accurate, reliable, and complete picture of the system's state.
  This is crucial for applications like navigation and robotics.

## Slide 142
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Data Compression
  DSP can be used to compress large amounts of sensor data, reducing storage requirements and speeding up transmission.
  This is especially important for IoT (Internet of Things) devices with limited bandwidth and memory.

## Slide 143
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Signal Enhancement
  Noise reduction, filtering, and signal smoothing improve sensor data quality by removing interference and unwanted components.
Feature Extraction and Pattern Recognition
  DSP helps extract meaningful information from raw sensor data, enabling applications such as object detection, motion tracking, and biometric recognition.

## Slide 144
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Motor and Stability Control
  Real-time DSP algorithms control motors and mechanical systems based on sensor feedback to maintain system stability and precision.
IoT and Automation
  DSP processes sensor data locally or remotely in IoT devices and industrial automation systems for predictive maintenance, monitoring, and control.

## Slide 145
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Advantages of DSP over Analog Signal Processing
Flexibility
  DSP is software-based, so algorithms can be easily changed or updated without modifying the hardware.
Accuracy and Repeatability
  Digital processing is not affected by component drift, temperature changes, or other environmental factors that can degrade analog circuits.
  This ensures that the same input always yields the same output.

## Slide 146
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Advanced Capabilities
  DSP allows for the implementation of complex algorithms and functions that are either impossible or too difficult to achieve with analog electronics.
Cost-Effectiveness
  For many applications, a single, general-purpose Digital Signal Processor (DSP) chip can replace multiple analog components, reducing the overall size and cost of the system.

## Slide 147
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Advantages of DSP in Sensor Systems
  High accuracy and precision.
  Flexible (algorithms can be changed in software).
  Enables smart sensors (self-calibration, decision-making).
  Supports IoT/AI integration.

## Slide 148
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common DSP Techniques Used in Sensor Applications
  Fast Fourier Transform (FFT) for spectral analysis.
  Adaptive filtering for noise cancellation.
  Kalman filtering for sensor fusion and state estimation.
  Wavelet transform for multi-resolution analysis.

## Slide 149
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 150
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Calibration and Compensation Techniques
Calibration
  Calibration is the process of adjusting a sensor's output to match a known reference standard. It is a fundamental step that establishes the relationship between the sensor's input and output under controlled conditions.
  This process helps to correct for systematic errors like offset (a non-zero output at zero input) and span/sensitivity errors (an incorrect slope of the output curve).

## Slide 151
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Static Calibration
  Measures sensor output at fixed, known input values.
  Creates a correction curve mapping sensor output to true inputs.
  Used for conditions that remain constant or change slowly, e.g., fixed temperature or pressure.
Dynamic Calibration
  Evaluates sensor performance under changing inputs.
  Assesses characteristics like frequency response and phase delay.
  Important for applications with fast or varying signals.

## Slide 152
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Two-Step Calibration
  Separates calibration of the sensor element from calibration of analog signal conditioning circuits.
  Improves accuracy by correcting errors introduced in both sensor and electronics.
Digital Calibration
  Employs DSP algorithms to compensate for sensor and ADC offsets, gains, and nonlinearities.
  Includes offset subtraction, gain scaling, and curve linearization.
  Enables flexible, real-time compensation without hardware changes.

## Slide 153
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Self-Calibration Techniques
Background Calibration
  Continuous, non-intrusive calibration during normal operation to adjust sensor drift automatically.
Foreground Calibration
  Scheduled calibration requiring stopping normal operation for precise adjustment.

## Slide 154
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Point-Based Calibration Methods
Single-Point Calibration
  Uses a single known reference.
  Mainly corrects offset errors by adjusting output to zero at a known zero-input.
  Simplest method but limited in addressing nonlinearities.
Two-Point Calibration
  Uses two known references at the low and high ends of range.
  Corrects offset and span (sensitivity) errors.
  Suitable for ensuring linear scaling across sensor range.

## Slide 155
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Multi-Point Calibration
  Uses three or more calibration points across the range.
  Corrects nonlinear sensor output with higher accuracy.
  Generates lookup tables or applies curve-fitting algorithms like polynomial regression.

## Slide 156
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Other Calibration Techniques
Curve Fitting
  Mathematical modeling (linear, polynomial, nonlinear regression) to map sensor outputs to true values, especially for nonlinear sensors.
Gravimetric Calibration
  For weighing sensors, compares outputs against known mass standards.
Electrical Calibration
  Compares sensor electrical parameters (voltage/current) against traceable electrical standards for precision.

## Slide 157
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Compensation
  Compensation is the method of counteracting errors that a sensor experiences due to environmental factors or other external influences that change over time, such as temperature, humidity, or aging.
  Unlike calibration, which is often done at a single point in time, compensation is a dynamic process that occurs continuously during operation.

## Slide 158
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Temperature Compensation
  Many sensors (RTDs, strain gauges, accelerometers) have outputs affected by temperature variations.
Methods:
    Use an auxiliary temperature sensor to measure ambient temperature.
    Apply hardware-based compensation by integrating components like thermistors in the sensor circuitry (e.g., Wheatstone bridge).
    Implement software-based algorithms or lookup tables to correct sensor output based on temperature error models.
    Use materials with low temperature coefficients to minimize temperature sensitivity.

## Slide 159
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Software-Based Compensation
  Builds mathematical models characterizing sensor behavior under varying conditions after calibration.
  Real-time processing of raw sensor data using algorithms like polynomial curve fitting or machine learning (e.g., neural networks).
  Offers flexibility and adaptability without hardware modification.

## Slide 160
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Hardware-Based Compensation
  Uses additional circuit components for direct error correction in the signal conditioning stage.
  Example: Incorporates thermistors in Wheatstone bridges to counteract temperature-induced resistance changes.
Hysteresis Compensation
  Minimizes output discrepancy caused by varying input history via algorithmic filtering or hardware techniques.

## Slide 161
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Nonlinearity Compensation
  Addresses nonlinear sensor output responses using polynomial curve fitting, lookup tables, or piecewise linear approximations.
  Essential for sensors like thermistors and photodiodes exhibiting inherent nonlinear characteristics.
Aging and Drift Compensation
  Compensates for sensor degradation and gradual output drift over time.
  Uses periodic recalibration or continuous software drift tracking for sustained accuracy.

## Slide 162
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Cross-Sensitivity Compensation
  Corrects interference from multiple parameters affecting the sensor output (e.g., humidity sensors also sensitive to temperature).
  Achieved by sensor fusion combining data from multiple sensors with algorithms.
Offset and Gain Adjustment
  Corrects zero-level (offset) errors and scales sensitivity (gain) to align output with standards.
  Often performed iteratively in analog sensors using zero and span adjustments.
  Digital systems may use baseline subtraction or digital offset correction (e.g., auto-zeroing in op-amps, ADC offset compensation).

## Slide 163
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 164
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Interfaces and Communication
A sensor interface is the connection that allows a sensor to communicate with other devices, such as a microcontroller or a computer.
It's the "bridge" that enables the data collected by the sensor to be read, processed, and used.
Sensor Interfaces
Serve as a bridge between sensors and attached devices.
Facilitate reading out information from sensor signals and provide suitable output signals for easy integration.
Examples include sensor interface ICs that read complex sensor inputs and output processing-friendly data.

## Slide 165
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Types of Sensor Interfaces
Sensor interfaces are broadly categorized based on how they transmit data:
Analog Interfaces
  These interfaces transmit a continuous electrical signal, such as voltage or current, that is directly proportional to the measured physical quantity.
  This raw data often requires signal conditioning (like amplification or filtering) and an analog-to-digital converter (ADC) to be read by a digital processing unit.

## Slide 166
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Analog sensors output a continuous voltage or current proportional to the measured parameter.
Voltage Output
  Example: LM35 temperature sensor (10 mV/°C).
  Microcontroller reads it using ADC (Analog-to-Digital Converter).
Current Output (4–20 mA standard in industry)
  Robust against noise and long-distance transmission.
  Requires resistor → converts current to voltage before ADC.
Resistance/Capacitance Change
  Example: LDR (resistance decreases with light).
  Usually converted into voltage using a voltage divider or Wheatstone bridge.

## Slide 167
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Digital Interfaces
  These interfaces transmit data as a discrete stream of 1s and 0s, which is a format easily understood by microcontrollers.
  They often include embedded electronics to perform tasks like signal conditioning and analog-to-digital conversion within the sensor itself.

## Slide 168
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Digital sensors provide output in discrete form (binary, serial data, or pulse). They often have built-in ADC + signal conditioning.
Simple Digital Output
  Output: HIGH/LOW (0 or 1).
  Example: PIR motion sensor, IR obstacle sensor.
Pulse/Frequency Output
  Sensor outputs a pulse train where frequency/duty cycle encodes the value.
  Example: Ultrasonic sensor (HC-SR04), PWM output humidity sensors.

## Slide 169
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Interfaces
  These interfaces transmit data without physical cables using various radio frequencies.
  They are a core component of the Internet of Things (IoT) and are used in applications where running wires is impractical.

## Slide 170
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Communication
  Communication is the process by which sensor data is transmitted from the sensor to a processing unit or network.
  This is achieved through various communication protocols, which are the set of rules that govern data exchange.

## Slide 171
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wired Protocols
  Low-Level Digital Communication: Protocols such as I2C, SPI, SENT, and HART are typically used for close-range sensor communication and provide reliable data transmission.
    I2C: Two-wire, low-speed communication, suitable for multiple sensors on the same bus.
    SPI: Four-wire, full-duplex, high-speed communication often used for sensors needing fast data transfer.
    SENT: Serial protocol for transmitting sensor data in automotive applications.

## Slide 172
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wired Protocols cond..
  Fieldbus Protocols: Used in industrial automation, including CAN (CANopen, CAN FD), Modbus RTU, and IO-Link.
  Industrial Ethernet: Higher-layer communication protocols over Ethernet for industrial sensor networks.
Advantages
  Secure, reliable, high-speed, and low latency.
Disadvantages
  Limited mobility, can be complex and costly to install, and can be vulnerable to physical damage.

## Slide 173
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Protocols
  Protocols like WiFi, Bluetooth, Zigbee, LoRaWAN allow sensors to transmit data without physical wiring.
  Wireless protocols enable flexibility and easy scalability but might have limitations in speed, interference, and power consumption.
Advantages
  Flexible, scalable, and easy to deploy.
Disadvantages
  Vulnerable to interference, security risks, and limited by battery life.

## Slide 174
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Common Serial Communication Protocols
UART: Used for simple, asynchronous sensor communication.
RS-232, RS-485: Widely adopted in industrial settings; RS-485 allows multiple sensors on the same bus.
USB: Used for higher-speed sensor connections.

## Slide 175
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Sensor Communication
Some sensors communicate over wireless standards:
  Infrared (IR) → Remote sensors.
  Bluetooth (BLE, BT Classic) → Wearables, IoT.
  Wi-Fi → ESP32-based sensors.
  Zigbee / LoRa → Long range, low power IoT applications.

## Slide 176
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Industrial Communication Standards
For robust, long-distance environments:
  RS-232 / RS-485 (differential signaling for noise immunity).
  CAN bus (used in automotive sensors).
  Modbus / Profibus / EtherCAT (industrial automation).

## Slide 177
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Choosing the Right Interface
  Short distance, low speed → I²C, UART.
  High speed, short distance → SPI.
  Long distance, noisy environment → 4–20 mA, RS-485, CAN.
  IoT/Wireless → Wi-Fi, BLE, Zigbee, LoRa.

## Slide 178
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Sensor Data Communication Characteristics
Data communication involves signal conversion, transmission, and interpretation by microcontrollers or processors.
Protocol selection depends on factors like data speed, wiring complexity, distance, power constraints, and system compatibility.
Protocols such as I2C and SPI are suited for embedded systems and short-distance communication, while CAN and Ethernet cater to more complex industrial needs.
Wireless protocols are preferred for IoT and smart devices where wiring is impractical.

## Slide 179
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Protocol Type | Advantage | Disadvantage | Typical Use Case
I2C | Simple wiring, multi-slave capability | Low speed, short distance | Temperature, humidity sensors
SPI | High speed, full duplex | More complex wiring | Accelerometers, gyroscopes
UART | Simple, asynchronous | Low data rate | Simple sensors
CAN | Robust, multi-device, industrial use | Complex protocol layers | Automotive, industrial networks
RS-485 | Multi-drop, long distance | Need software protocol for data | Industrial sensors
Wireless (WiFi/Bluetooth) | No wiring, flexible | Power consumption, interference | IoT, smart home, remote sensors
Table of Sensor Communication Protocols

## Slide 180
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Protocol | Wires | Speed | Topology | Addressing | Use Cases | Pros | Cons
I²C | SDA, SCL | ~100 kbps to 3.4 Mbps | Multi-master, multi-slave | Yes | MPU6050, EEPROMs, RTCs | Simple wiring, supports many devices | Slower, limited distance
SPI | MISO, MOSI, SCK, CS | Up to 10+ Mbps | Single master, multiple slaves | No (uses CS lines) | SD cards, ADCs, displays | Very fast, full-duplex | More pins, no native addressing
UART | TX, RX | ~9600 to 1 Mbps | Point-to-point | No | GPS modules, Bluetooth HC-05 | Simple, widely supported | No multi-device support, slower
Sensor Communication Protocols Comparison

## Slide 181
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication Protocols
Protocol | Wires | Speed | Use Case
UART | 2 | Up to 115200 bps | Simple serial communication
I²C | 2 | 100Kbps–400Kbps | Multi-device setups
SPI | 4 | Up to several Mbps | Fast, short-distance comms
CAN | 2 | 1 Mbps typical | Automotive, industrial systems

## Slide 182
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Analog and Digital Interfaces
  Analog and digital interfaces in sensors refer to the methods by which sensors communicate their output signals to other devices, such as microcontrollers or data acquisition systems.
  Analog interfaces use a continuous signal, while digital interfaces use discrete, binary values
.

## Slide 183
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Analog Interfaces in Sensors
  Analog sensors output a continuous signal, usually a voltage, that varies proportionally to the measured physical quantity (e.g., temperature, pressure, light intensity).
  This continuous analog signal is susceptible to noise and requires signal conditioning stages such as amplification, filtering, and offset removal before being converted to a digital format.
  Analog-to-digital converters (ADCs) are used to translate these continuous signals into discrete digital values for processing by microcontrollers or computers.

## Slide 184
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Analog Interfaces in Sensors Cond..
  Key considerations in analog interfacing include precision, sampling rate, noise susceptibility, and linearity.
  Analog outputs provide information in real time and allow high resolution depending on the ADC bit depth.

## Slide 185
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Examples
  Temperature sensor (LM35 → 10 mV/°C).
  LDR (Light Dependent Resistor) → resistance changes with light.
  Potentiometer → varying resistance → variable voltage.
Advantages
  Simple design, low cost.
  High resolution depending on ADC.
Disadvantages
  Needs extra circuitry (ADC, filters).
  Sensitive to interference and drift.

## Slide 186
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Digital Interfaces in Sensors
  Digital sensors output data in a discrete, digital form that microcontrollers can directly read without needing ADCs.
  These sensors often use communication protocols such as I2C, SPI, UART, 1-wire, or USB to transmit data.
  Digital signals have higher immunity to noise, can simplify wiring and interfacing, and support error checking and robust communication.
  Digital interfaces facilitate straightforward integration with digital systems and often include built-in signal processing.

## Slide 187
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Digital Interfaces in Sensors Cond..
  Examples include sensors like the DHT11 for temperature/humidity, which communicate digital data directly.
  Important aspects for digital interfaces include logic level compatibility, voltage compatibility, signal timing, and communication protocol.

## Slide 188
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Examples
  DHT11/DHT22 (temperature & humidity → single-wire digital output).
  MPU6050 (accelerometer + gyroscope → I²C/SPI).
  Ultrasonic sensor HC-SR04 (digital trigger/echo pulses).
Advantages
  Easier integration with microcontrollers.
  Can transmit over long distances reliably.
  Often provides extra features (calibration, self-test).
Disadvantages
  More expensive than analog.
  Requires protocol handling in software.

## Slide 189
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Table of Analog vs. Digital Interfaces
Interface Type | Signal Nature | Pros | Cons | Typical Sensor Examples
Analog | Continuous voltage or current | High fidelity, direct physical representation | Noise susceptibility, requires ADC for digital use | Thermocouples, RTDs, strain gauges
Digital | Discrete digital values | Noise immune, easy digital integration | Quantization error, limited resolution | Digital pressure, temperature sensors, MEMS sensors

## Slide 190
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Differences
Aspect | Analog Interface | Digital Interface
Signal Type | Continuous voltage/current | Discrete digital data
Processing | Requires ADC for digital processing | Directly readable by microcontrollers
Noise Susceptibility | More susceptible to noise | Less susceptible, higher noise immunity
Communication | Simple wiring but sensitive to noise | Uses protocols like I2C, SPI, UART
Complexity | Needs signal conditioning and ADC | Built-in processing, simpler integration
Resolution | Depends on sensor and ADC bit depth | Limited by digital protocol and sensor design

## Slide 191
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Sensor Network (WSN)
  A Wireless Sensor Network (WSN) is a distributed network of small, low-power devices called sensor nodes.
  These nodes are equipped with sensors, processors, and wireless transmitters to collect and share data about environmental conditions like temperature, humidity, motion, or pressure
  A Wireless Sensor Network (WSN) is a network of spatially distributed, autonomous devices called sensor nodes that use sensors to cooperatively monitor and record physical or environmental conditions and then forward the collected data wirelessly to a central location.

## Slide 192
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Sensor Network (WSN)

## Slide 193
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Sensor Network (WSN)

## Slide 194
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Wireless Sensor Network (WSN)

## Slide 195
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Components of a WSN
  The key components of a Wireless Sensor Network (WSN) include several integral parts, each serving a specific role to ensure efficient sensing, data transmission, and processing:
Sensor Nodes:
  Small, low-power devices equipped with sensors that measure physical phenomena like temperature, light, pressure, humidity, or motion.
  Each node contains a microcontroller to locally process and store collected data.
  A transceiver module (e.g., Wi-Fi, Bluetooth, Zigbee) enables wireless communication between nodes and with other parts of the network.
  Powered by batteries, often extended by energy harvesting methods such as solar panels to prolong network lifetime.

## Slide 196
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Components of a WSN Cond..
Communication Layer:
  Facilitates wireless data transmission within the network using protocols such as radio waves, ZigBee, Wi-Fi, or Bluetooth.
  Ensures reliable and efficient communication between sensor nodes and the gateway or base station.
Gateways/Base Stations:
  Serve as a bridge between the WSN and external networks like the internet.
  Collect data from sensor nodes, aggregate, and forward it to central servers or user platforms for further analysis and storage.

## Slide 197
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Components of a WSN Cond..
.
Middleware and Software:
  Software layers handle data aggregation, processing, and interpretation, converting raw sensor input into meaningful information for users and applications.
Actuators (Optional):
  Devices that perform actions based on sensor data, enabling bi-directional communication and control.
  Example: In a smart irrigation system, an actuator might turn on sprinklers when soil moisture sensed by nodes falls below a threshold.

## Slide 198
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Components of a WSN Cond..
.
Central Server/User Platform:
  Centralized location, either local or cloud-based, that aggregates, processes, stores, and analyzes data collected through the WSN.
  Provides interfaces for monitoring, visualization, and control for end users or automated systems.
Together, these components form a comprehensive ecosystem that allows a Wireless Sensor Network to sense, communicate, control, and provide actionable insights for various applications

## Slide 199
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
WSN Architecture Layers:

## Slide 200
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
WSN Architecture Layers:
  Physical Layer: Deals with wireless communication hardware, radio transmission, and sensor connectivity.
  Data Link Layer: Ensures reliable data transfer between nodes and handles MAC protocols to manage access to the communication medium.
  Network Layer: Responsible for routing and forwarding packets efficiently from sensor nodes to the base station.
  Transport Layer: Ensures end-to-end reliability, data integrity, and communication management.
  Application Layer: Interfaces with users and processes sensor data according to application needs.

## Slide 201
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication Protocols
Zigbee (IEEE 802.15.4) – low power, short range.
Bluetooth Low Energy (BLE) – wearable & mobile sensors.
LoRa/LoRaWAN – long range, low power.
Wi-Fi – higher data rate but power-hungry.
6LoWPAN – IPv6 over low-power wireless networks.

## Slide 202
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Network Topologies in WSN:
Bus Topology: Nodes share a common communication line.
Star Topology: All nodes connect to a central master node.
Tree Topology: Nodes arranged hierarchically.
Mesh Topology: Nodes connect with multiple other nodes, providing redundancy and robustness.

## Slide 203
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Network Topologies in WSN:

## Slide 204
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Advantages of WSN
  Cost-effective due to low-cost sensors.
  Wireless and easy to deploy.
  Energy-efficient for long-term operation.
  Scalable and flexible.
  Enables real-time monitoring of environments.

## Slide 205
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
WSN Applications

## Slide 206
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
WSN Applications
WSNs have a wide range of applications across various industries:
Environmental Monitoring
  Detecting and tracking forest fires, monitoring air and water quality, and surveying wildlife habitats.
Agriculture
  Monitoring soil moisture, temperature, and humidity to optimize irrigation and crop yield.
Industrial Automation
  Machine health monitoring, predictive maintenance, and control of industrial processes.

## Slide 207
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
WSN Applications Cond..
Healthcare
  Remote patient monitoring, tracking the movement of patients and medical staff, and managing hospital assets.
Smart Cities
  Managing traffic, monitoring structural health of bridges and buildings, and optimizing energy consumption in public spaces.
Military:
  Battlefield surveillance, equipment tracking, and detection of chemical or biological threats.

## Slide 208
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Challenges in WSN
Despite their utility, WSNs face several significant challenges:
Energy Efficiency
  Most sensor nodes are battery-powered and operate in remote locations, making battery replacement difficult or impossible.
  Minimizing power consumption through efficient communication protocols and sleep modes is crucial.
Scalability
  A WSN may consist of hundreds or even thousands of nodes.
  Designing the network to handle this scale and ensure reliable data routing is a complex task.

## Slide 209
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Challenges in WSN Cond..
Security
  Since communication is wireless, WSNs are vulnerable to various security threats, including data interception, node capture, and denial-of-service attacks.
  Ensuring data confidentiality and integrity is a major concern.
Reliability and Fault Tolerance
  Sensor nodes can fail due to harsh environmental conditions or power depletion.
  The network must be able to tolerate these failures and maintain its functionality.
Data Management
  The sheer volume of data generated by a large WSN requires efficient data aggregation, processing, and storage techniques to avoid overwhelming the network and its central server.

## Slide 210
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication protocols
  Communication protocols are sets of rules that allow two or more electronic devices to exchange data.
  In embedded systems, three of the most common serial communication protocols are I²C, SPI, and UART.
  Each has unique characteristics that make it suitable for different applications.

## Slide 211
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
I2C (Inter-Integrated Circuit)
  I2C is a synchronous, multi-master, multi-slave serial communication protocol developed by Philips.
  It uses only two wires: one for clock (SCL) and one for data (SDA).
  Devices are assigned a unique 7-bit or 10-bit address, allowing a single master to communicate with multiple slaves on the same bus.
  I2C is great for short-distance communication between components on a single circuit board, like communicating with EEPROMs, real-time clocks, and sensors.

## Slide 212
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
I2C (Inter-Integrated Circuit)

## Slide 213
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
I2C (Inter-Integrated Circuit)
Key Features
Two-wire interface:
  This is a major advantage, as it simplifies hardware and reduces the number of pins required on microcontrollers.
Half-duplex communication:
  Data can be sent and received on the same line, but not at the same time.
Multi-master/multi-slave support:
  Multiple master and multiple slave devices can be connected on the same bus.

## Slide 214
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
I2C (Inter-Integrated Circuit)
Key Features
Addressing:
  The address-based system allows the master to communicate with multiple slaves individually.
Open-drain:
  Both the SDA and SCL lines are "open-drain," requiring pull-up resistors to maintain a high logic state when no device is pulling them low.
  This design prevents conflicts if multiple devices try to drive the bus at the same time.

## Slide 215
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 216
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 217
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 218
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication process
  Start condition: The master device initiates communication by pulling the SDA line low while the SCL line is high.
  Addressing: The master sends the 7-bit or 10-bit address of the target slave device, followed by a read/write bit to indicate the direction of data transfer.
  Acknowledge (ACK): The addressed slave device pulls the SDA line low to acknowledge that it has received its address. If the slave doesn't acknowledge, the master can generate a stop condition.
  Data transfer: The master or slave (depending on the read/write bit) transfers 8 bits of data. After each byte, the receiving device must send an acknowledge bit.
  Stop condition: The master ends the communication by pulling the SDA line high while the SCL line is high.

## Slide 219
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Characteristics
  Multi-master support: Multiple masters can exist on the same bus, but only one can control the bus at a time. A process called "arbitration" handles conflicts if two masters try to communicate at the same time.
  Simple wiring: Only two wires are needed for communication, which simplifies circuit design.
  Cost-effective: The protocol is simple and requires minimal hardware, making it a low-cost solution.
  Moderate speed: It's faster than protocols like UART but slower than SPI. Standard speeds include 100 kbps (Standard Mode), 400 kbps (Fast Mode), and 1 Mbps (Fast-mode Plus).
  Addressing: Each device has a unique address, allowing multiple devices to share the same bus.

## Slide 220
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Mode | Speed
Standard | 100 kbps
Fast | 400 kbps
Fast Plus | 1 Mbps
High Speed | 3.4 Mbps
Ultra Fast | 5 Mbps (rare)
I²C Speed Modes

## Slide 221
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
I2C Protocol
Advantages
  It supports various master devices.
  It offers multi-slave and multi-master communication.
  This protocol is flexible and adaptable too.
Disadvantages
  I2C is a bit slower protocol because of the need for pull-up resistors.
  It takes up more space.
  The architecture is more complex with the increasing number of devices.
  This protocol is half-duplex, which is quite problematic and requires different devices for complete communication.

## Slide 222
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 223
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI (Serial Peripheral Interface)
  SPI is a synchronous, full-duplex serial communication protocol.
  It's often used for short-distance communication, primarily in embedded systems.
  It uses a master-slave architecture and requires four wires:
    SCLK (Serial Clock): The clock signal generated by the master.
    MOSI (Master Out, Slave In): Data from the master to the slave.
    MISO (Master In, Slave Out): Data from the slave to the master.
    SS (Slave Select) or CS (Chip Select): A signal used by the master to enable communication with a specific slave.
SPI is faster than I2C and is commonly used for communicating with flash memory, ADC (Analog-to-Digital Converters), DAC (Digital-to-Analog Converters), and SD card modules.

## Slide 224
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI (Serial Peripheral Interface)
Key Features
Four-wire interface: SCLK, MOSI, MISO, and SS.
Synchronous: Uses a shared clock signal.
Full-duplex: Data can be sent and received simultaneously.
Single-master, multiple-slaves: One master communicates with one or more slaves (one at a time using the SS line).
High speed: Can operate at very high speeds, often in the tens of MHz.
No acknowledgment: There is no built-in acknowledgment mechanism.

## Slide 225
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI (Serial Peripheral Interface)

## Slide 226
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore

## Slide 227
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication process
  The master device pulls the SS line for the desired slave low to select it.
  The master generates the clock signal on the SCLK line.
  Simultaneously, the master sends data on the MOSI line, and the selected slave sends data back on the MISO line. This is the full-duplex nature of SPI, as data can be sent and received at the same time.
  Data is transferred bit by bit, synchronized with the SCLK.
  After the transfer is complete, the master pulls the SS line high to deselect the slave.

## Slide 228
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Characteristics
  High Speed: SPI is significantly faster than protocols like I²C because it doesn't have the overhead of addressing and acknowledgments. It can reach speeds in the tens of MHz.
  Full-Duplex: Data can be sent and received at the same time, increasing throughput.
  Simple: The protocol is very simple with no complex addressing or arbitration logic.
  Single Master: The bus can only have one master, though it can communicate with multiple slaves.
  More Wires: A major drawback is the need for a dedicated Slave Select line for each slave, which increases the number of required wires as more devices are added.

## Slide 229
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI Protocol Operating Modes
The SPI protocol can operate in various modes, including:
  Mode 0: In Mode 0, the clock signal is low when idle, and data is sampled on the rising edge of the clock signal.
  Mode 1: In Mode 1, the clock signal is low when idle, and data is sampled on the falling edge of the clock signal.
  Mode 2: In Mode 2, the clock signal is high when idle, and data is sampled on the falling edge of the clock signal.
  Mode 3: In Mode 3, the clock signal is high when idle, and data is sampled on the rising edge of the clock signal.

## Slide 230
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI Protocol
Advantages
  Supports full duplex communication.
  Simple and fast data transmission rate.
  Offers simple software implications.
  No, start and stop bits allow continuous data transmission with no interruptions.
  MOSI and MISO allow simultaneous data send and receive operations.
  The use of a master clock doesn't require precious oscillators.

## Slide 231
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
SPI Protocol
Disadvantages
  More use of slave devices complicates the wiring.
  It has a single master device.
  Limits the number of slave's devices to connect with the Master.
  No error check mechanism.
  Don't have an acknowledgment line of data receiving a message.

## Slide 232
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
UART (Universal Asynchronous Receiver/Transmitter)
  UART is an asynchronous communication protocol, meaning it doesn't use a clock signal to synchronize the sender and receiver. Instead, it relies on both devices having a pre-agreed baud rate (the rate at which data is transmitted).
  It's a point-to-point protocol, meaning it's primarily used for communication between two devices.
  It uses two wires:
    TX (Transmitter): The line used for sending data.
    RX (Receiver): The line used for receiving data.
  UART is widely used for communication between a microcontroller and a computer (via a USB-to-serial converter), GPS modules, Bluetooth modules, and other peripherals.

## Slide 233
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
UART (Universal Asynchronous Receiver/Transmitter)

## Slide 234
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
UART works in three various ways
  Simplex: In a simplex system, data is transmitted in only one direction.
  Half-duplex: In a half-duplex system, data is transmitted in both directions but not simultaneously.
  Full-duplex: In a full-duplex system, data is simultaneously transmitted in both directions.

## Slide 235
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Communication process
The data is sent in packets or frames, which consist of:
  Start Bit: A single bit that signals the beginning of a new data frame. It is a transition from a high voltage level to a low voltage level.
  Data Bits: The actual data being transmitted, typically 5 to 9 bits long. The least significant bit (LSB) is usually sent first.
  Parity Bit (Optional): An optional bit used for error checking. It helps the receiver detect if a single bit has been corrupted during transmission.
  Stop Bit(s): One or two bits that signal the end of the data frame. They are a transition back to a high voltage level.

## Slide 236
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Characteristics
  Asynchronous: No clock signal is needed, which simplifies the wiring. However, both devices must agree on the same baud rate.
  Full-Duplex: UART allows for simultaneous two-way communication since it has separate transmit and receive lines.
  Simple: The protocol is straightforward to implement and requires minimal hardware overhead.
  Limited: UART is generally used for point-to-point communication between two devices and is not suitable for multi-master or multi-slave configurations like I²C or SPI. Its speed is also much lower than SPI.

## Slide 237
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
UART (Universal Asynchronous Receiver/Transmitter)
Key Features
Two-wire interface: TX and RX.
Asynchronous: No shared clock signal.
Half-duplex: Data is sent in one direction at a time (unless both devices can transmit and receive simultaneously).
Point-to-point: Typically used for one-to-one communication.
Variable speed: The baud rate must be set identically on both the transmitter and receiver.
Data framing: Each byte of data is framed with a start bit and a stop bit for synchronization.

## Slide 238
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
UART Protocols
Advantages
  It only uses two lines or wires helping to clean circuitry
  It doesn't require a clock signal.
  It has a parity bit for error checking.
  It is an easy and widely used method of communication.
Disadvantages
  It has a limited data size of 9 bits only.
  It doesn't support multiple Master and slave devices.
  The baud rate or the data transmission speed should be below 10 % or each other.
  The data transmission rate is lower compared to the remaining protocols.

## Slide 239
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Features | UART | SPI | I2C
Full Form | Universal Asynchronous Receiver/Transmitter | Serial Peripheral Interface | Inter-Integrated Circuit
Pin Designations | TxD: Transmit Data RxD: Receive Data | SCLK: Serial Clock MOSI: Master Output, Slave Input MISO: Master Input, Slave Output SS: Slave Select | SDA: Serial Data SCL: Serial Clock
Data rate | The maximum data rate supported is about 230 Kbps to 460 Kbps. | Usually supports about 10 Mbps to 20 Mbps | I2C supports 100 kbps, 400 kbps, and 3.4 Mbps. Some variants also support 10 Kbps and 1 Mbps.
Type of communication interfaces | Asynchronous | Synchronous | Synchronous
Distance | Lower about 50 feet | highest | Higher
Master Device | One | One | One or more than One
Clock | No use of Common Clock signal. Both devices will use their independent clocks. | There is one common serial clock signal between master and slave devices. | There is a common clock signal between multiple masters and multiple slaves.

## Slide 240
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Features | UART | SPI | I2C
Hardware complexity | lesser | less | more
Protocol | For 8 bits of data, one start bit and one stop bit are used. | Each manufacturer has got their own specific protocols to communicate with peripherals. Hence, a datasheet is a must-to-know read/write the protocol for SPI communication to be established. | It uses start and stops bits. It uses an ACK bit for every 8 bits of data which indicates whether data has been received or not.
Software addressing | There is no need for addressing since this is a one-to-one connection between two devices. | Any slave connected with the master is addressed by a slave select line. A master device will have 'n' slave select lines for 'n' slaves. | Any slave connected with the master is addressed by a slave select line. A master device will have 'n' slave select lines for 'n' slaves.

## Slide 241
Industrial IoT and Industry 4.0
Tektork Private Limited, Coimbatore
Thank You